Industrial photogrammerty

In this exercise we load a video, try to identify in the video the movement of a ball and mark the ball with cross and add its coordinates
-start IDE: Computer->O:\Software\Programmierung\QT\Tools\QtCreator\bin->qtcreator.exe
- create a new project motiondetect in folder opencvproj/UE_4
- set mode down left from debug to release
- in the .pro file add the location of the include files and of the dllsbelow
FORMS += \
        mainwindow.ui:

INCLUDEPATH += U:\opencv340\include

LIBS += U:\opencv340\bin\libopencv_core340.dll
LIBS += U:\opencv340\bin\libopencv_highgui340.dll
LIBS += U:\opencv340\bin\libopencv_imgcodecs340.dll
LIBS += U:\opencv340\bin\libopencv_imgproc340.dll
LIBS += U:\opencv340\bin\libopencv_videoio340.dll
LIBS += U:\opencv340\bin\libopencv_video340.dll
LIBS += U:\opencv340\bin\libopencv_features2d340.dll
LIBS += U:\opencv340\bin\libopencv_calib3d340.dll
 ----------------------------------------------------------------

- under sources open the file mainwindow.cpp
- over line add:

#include "mainwindow.h"
#include "ui_mainwindow.h"
#include <QMainWindow>
//opencv
#include "opencv2/imgcodecs.hpp"
#include "opencv2/imgproc.hpp"
#include "opencv2/videoio.hpp"
#include <opencv2/highgui.hpp>
#include <opencv2/video.hpp>
//C++
#include <iostream>
#include <sstream>
using namespace std;
using namespace cv;
//our sensitivity value to be used in the absdiff() function
const static int SENSITIVITY_VALUE = 20;
//size of blur used to smooth the intensity image output from absdiff() function
const static int BLUR_SIZE = 10;
//we'll have just one object to search for
//and keep track of its position.
int theObject[2] = {0,0};
//bounding rectangle of the object, we will use the center of this as its position.
Rect objectBoundingRectangle = Rect(0,0,0,0);
 ----------------------------

- under addthe function processVideo();
-under Headers mainwindow.h doubleclick and completely change content to:

#ifndef MAINWINDOW_H
#define MAINWINDOW_H
#include <QMainWindow>
//opencv
#include "opencv2/imgcodecs.hpp"
#include "opencv2/imgproc.hpp"
#include "opencv2/videoio.hpp"
#include <opencv2/highgui.hpp>
#include <opencv2/video.hpp>
using namespace cv;
namespace Ui {
class MainWindow;
}
class MainWindow : public QMainWindow
{
    Q_OBJECT
public:
    explicit MainWindow(QWidget *parent = 0);
    ~MainWindow();
    void processVideo();
    std::string intToString(int number);
    void searchForMovement(Mat thresholdImage, Mat &cameraFeed);
private:
    Ui::MainWindow *ui;
};
#endif // MAINWINDOW_H
 ----------------------------------------------------
- at the end of mainwindow.cpp add our function code for processVideo():

void MainWindow::processVideo(){
    //some boolean variables for added functionality
    //these two can be toggled by pressing 'd' or 't'
    bool debugMode = false;
    bool trackingEnabled = false;
    //pause and resume code
    bool pause = false;
    //set up the matrices that we will need
    //the two frames we will be comparing
    Mat frame1,frame2;
    //their grayscale images (needed for absdiff() function)
    Mat grayImage1,grayImage2;
    //resulting difference image
    Mat differenceImage;
    //thresholded difference image (for use in findContours() function)
    Mat thresholdImage;
    //video capture object.
    VideoCapture capture;
    while(1){
        //we can loop the video by re-opening the capture every time the video	reaches its last frame
        capture.open("U://opencvProjEng//opencvProj//TRACKMOTIONBALL//bounce.avi");
        if(!capture.isOpened()){
        cout<<"ERROR ACQUIRING VIDEO FEED\n";
        getchar();
        return;
        }
//check if the video has reach its last frame.
//we add '-1' because we are reading two frames from the video at a	time.
//if this is not included, we get a memory error! while(capture.get(CV_CAP_PROP_POS_FRAMES)<capture.get(CV_CAP_PROP_FRAME_COUNT)-1){
        //read first frame
        capture.read(frame1);
        //convert frame1 to gray scale for frame differencing
        cv::cvtColor(frame1,grayImage1,COLOR_BGR2GRAY);
        //copy second frame
        capture.read(frame2);
        //convert frame2 to gray scale for frame differencing
        cv::cvtColor(frame2,grayImage2,COLOR_BGR2GRAY);
        //perform frame differencing with the sequential images. This will	output an "intensity image"
        //do not confuse this with a threshold image, we will need to	perform thresholding afterwards.
        cv::absdiff(grayImage1,grayImage2,differenceImage);
        //threshold intensity image at a given sensitivity value	cv::threshold(differenceImage,thresholdImage,SENSITIVITY_VALUE,
255,THRESH_BINARY);

        //show the difference image and threshold image
        cv::imshow("Difference Image",differenceImage);
        cv::imshow("Threshold Image", thresholdImage);
        //blur the image to get rid of the noise. This will output an	intensity image
        cv::blur(thresholdImage,thresholdImage,	cv::Size(BLUR_SIZE,BLUR_SIZE));

        //threshold again to obtain binary image from blur output
cv::threshold(thresholdImage,thresholdImage,SENSITIVITY_VALUE,
255,THRESH_BINARY);

        //show the threshold image after it's been "blurred"
        imshow("Final Threshold Image",thresholdImage);

        MainWindow::searchForMovement(thresholdImage,frame1);
        //flip(frame1, frame1, 0); //turn image upside down
        //show our captured frame
        imshow("Frame1",frame1);
        //check to see if a button has been pressed.
        //this 10ms delay is necessary for proper operation of this program
        //if removed, frames will not have enough time to referesh and a	blank
        //image will appear.
        switch(waitKey(10)){
        case 27: //'esc' key has been pressed, exit program.
        return;
        case 116: //'t' has been pressed. this will toggle tracking
        trackingEnabled = !trackingEnabled;
        if(trackingEnabled == false) cout<<"Tracking disabled."<<endl;
        else cout<<"Tracking enabled."<<endl;
        break;
        case 100: //'d' has been pressed. this will debug mode
        debugMode = !debugMode;
        if(debugMode == false) cout<<"Debug mode disabled."<<endl;
        else cout<<"Debug mode enabled."<<endl;
        break;
        case 112: //'p' has been pressed. this will pause/resume the code.
        pause = !pause;
        if(pause == true){ cout<<"Code paused, press 'p' again to	resume"<<endl;
        while (pause == true){
        //stay in this loop until
        switch (waitKey()){
        //a switch statement inside a switch statement? Mind	blown.
        case 112:
        //change pause back to false
        pause = false;
        cout<<"Code resumed."<<endl;
        break;
        }
        }
        }
        }
        }
        //release the capture before re-opening and looping again.
        capture.release();
    }
    return;
}

 --------------------------------------------
- add below that a small helper function that converts a number into a string:

//int to string helper function
string MainWindow::intToString(int number){
    //this function has a number input and string output
    std::stringstream ss;
    ss << number;
    return ss.str();
}
 --------------------------------------------
-add below a function that is looking for movement by subtracting the intensities per pixel of two subsequent images + blurring + thresholding:

void MainWindow::searchForMovement(Mat thresholdImage, Mat &cameraFeed){
    //notice how we use the '&' operator for the cameraFeed. This is because we wish
    //to take the values passed into the function and manipulate them, rather than just working with a copy.
    //eg. we draw to the cameraFeed in this function which is then displayed in the main() function.
    bool objectDetected=false;
    Mat temp;
    thresholdImage.copyTo(temp);
    //these two vectors needed for output of findContours
    vector< vector<Point> > contours;
    vector<Vec4i> hierarchy;
    //find contours of filtered image using openCV findContours function
    //findContours(temp,contours,hierarchy,CV_RETR_CCOMP,CV_CHAIN_APPROX_SIMPLE	);// retrieves all contours
    findContours(temp,contours,hierarchy,CV_RETR_EXTERNAL,CV_CHAIN_APPROX_SIMPLE	);// retrieves external contours
    //if contours vector is not empty, we have found some objects
    if(contours.size()>0)objectDetected=true;
    else objectDetected = false;
    if(objectDetected){
        //the largest contour is found at the end of the contours vector
        //we will simply assume that the biggest contour is the object we are	looking for.
        vector< vector<Point> > largestContourVec;
        largestContourVec.push_back(contours.at(contours.size()-1));
        //make a bounding rectangle around the largest contour then find its	centroid
        //this will be the object's final estimated position.
        objectBoundingRectangle = boundingRect(largestContourVec.at(0));
        int xpos = objectBoundingRectangle.x+objectBoundingRectangle.width/2;
        int ypos = objectBoundingRectangle.y+objectBoundingRectangle.height/2;
        //update the objects positions by changing the 'theObject' array values
        theObject[0] = xpos , theObject[1] = ypos;
    }

    //make some temp x and y variables so we dont have to type out so much
    int x = theObject[0];
    int y = theObject[1];
    //draw some crosshairs on the object
    circle(cameraFeed,Point(x,y),20,Scalar(0,255,0),2);
    line(cameraFeed,Point(x,y),Point(x,y-25),Scalar(0,255,0),2);
    line(cameraFeed,Point(x,y),Point(x,y+25),Scalar(0,255,0),2);
    line(cameraFeed,Point(x,y),Point(x-25,y),Scalar(0,255,0),2);
    line(cameraFeed,Point(x,y),Point(x+25,y),Scalar(0,255,0),2);
 putText(cameraFeed,"Tracking object at (" + intToString(x)	+","+intToString(y)+")",Point(0,0),1,1,Scalar(255,0,0),2);
}
 ---------------------------------------

- Datei → alles speichern → build (hammer)
-copy all the dlls from the QT5dlls_r230 folder into the newly built release folder build_motiondetect_Desktop...
execute your motiondetect.exe file
- four windows should appear: